## Slide 1
Popularity and prevalence of gas exchange data processing
methods in peer-reviewed literature: a scoping review
Anton Hesse, MS
Cardiopulmonary exercise testing (CPET) is the gold standard for non-invasively measuring cardiorespiratory fitness and is popular in many fields.
CPET analyzes expired gases, usually generating one data point per breath (breath-by-breath). Consequentially, this data requires processing before later analysis because respiratory variability is much higher than the underlying metabolism it reflects.
There is no universal method to process breath-by-breath data, and previous research shows that different approaches can affect downstream results.
There is little research on the popularity of different data processing methods and how often they are described in peer-reviewed literature.
Introduction
Methods
Figure 1. Label in 28pt Calibri.
v
v
v
This scoping review follows the Preferred Reporting Items for Systematic reviews and Meta-Analyses extension for Scoping Reviews
Download a list of original, peer-reviewed articles from 3 databases
Download full-text articles
Convert articles to txt format
Normalize article text for easier analysis
Screen articles not satisfying search criteria
Use regular expressions to find studies that collected data breath-by-breath
Use regular expressions to extract text regarding outliers, interpolation, and data averaging
The prevalence of data processing reporting for variable breath-by-breath data is low
The most common outlier limit is ± 3 or 4 standard deviations
1-second and linear interpolation are the most prevalent
Time-based bin averages, especially every 30 seconds, are the most common breath-by-breath averaging method
Results
Of the 7119 articles analyzed, 328 (4.6%) described outlier removal, 470 (6.6%) described interpolation, and an estimated 4366 (61.3%) described averaging methods.
The most popular outlier cutoffs are mean ± 3 or 4 SD (40.5% and 50.6%, respectively).
When documented, the dominating interpolation time frame and procedure were one second (94.7%) and linear interpolation (92.8%), respectively.
Time-based bin averages (84.6%) were the most popular averaging methods.
30-second bin averages are the most common averaging methods
Discussion
Very few papers describe their outlier removal and interpolation methods
Only 60% of papers describe their averaging methods, despite known implications of averaging on VO2max
The lack of interpolation methods is less concerning because this applies to mainly VO2 kinetics studies
More research should include descriptions of breath-by-breath data processing to improve reproducibility and comparability between studies. This is especially important for data averaging.